# LK Series Specifications

## 1.0	Scope

### 1.1	This specification in combination with pump data sheets identifies the minimum requirements for diaphragm metering pumps.

## 2.0	Definitions

### 2.1	Mechanically Actuated Diaphragm Pump - a positive displacement diaphragm-metering pump in which there is a direct coupling mechanism between the diaphragm and the motor.

## 3.0	General

### 3.1   Output volume shall be adjustable while pump is in operation.

### 3.2	Weight of pump as installed shall not exceed 63 pounds.

### 3.3	Pump shall fit within a rectangular volume 17” long by 9” wide by 21” high.

## 4.0	Drive

### 4.1	The mechanically actuated diaphragm metering pump mechanism shall be totally enclosed       with no exposed moving parts.

### 4.2 	The pump drive shall utilize a lost motion design.  The rotation of the motor shall be reduced by means of a worm and wheel.  The rotation shall be converted to a reciprocating motion by means of a dual cam, and a spring back mechanism including the worm wheel, shaft, slider, and spring.

### 4.3	The pump drive shall be oil-bath lubricated

### 4.4	The diaphragm shall be mechanically connected to the pump drive.  There shall be no hydraulic oil backing of the diaphragm to ensure there is no contamination of the process fluid in the event of a diaphragm failure.

### 4.5	Pump drive shall be by 1/3 HP, NEMA 42C electric motor.

### 4.6	Metering pump shall be capable of pumping a maximum of (q) GPH against a maximum pressure of (p) PSI. (q and p from Table 1)

### 4.7	Stroke length shall be adjustable from 10% to 100% by means of a micrometer dial.

### 4.8	An optional DC drive shall provide for external control by a 4-20mA input signal.  The control shall be NEMA 4X and shall include a manual/external switch.

## 5.0	Materials of construction

### 5.1	Pump housing shall be epoxy painted aluminum.

### 5.2	All exposed fasteners shall be stainless steel.

### 5.3	Liquid end materials shall be as shown in Table 2.

## 6.0	Shop tests

### 6.1	All pumps shall pass manufacturer’s standard performance test.

##### Table 1		Capacity/Pressure Rating

| Model | Capacity | Maximum Pressure PSI (MPa) | Stroke speed (spm) | Connection NPT | Max Viscosity cps |
| --- | --- | --- | --- | --- | --- |
|  | 50Hz (l/h) | 60Hz (GPH) | PVC/PVDF | SS | 50Hz | 60Hz | PVC/PVDF | SS |  |
| LKN32 | 30 | 9.5 | 150 (1) | 225 (1.5) | 96 | 116 | ½” | ½” | VC: 300 TC: 300 VH: 500 VS: 1000 S6: 1000 |
| LKN45 | 50 | 15.9 | 150 (1) | 225 (1.5) | 48 | 58 | ½” | ½” |  |
| LKN47 | 100 | 31.8 | 120 (0.8) | 120 (0.8) | 96 | 116 | ½” * | ½” |  |
| LKN55 | 168 | 53.4 | 75 (0.5) | 75 (0.5) | 48 | 58 | 1” | 1” |  |
| LKN57 | 360 | 114.3 | 45 (0.3) | 45 (0.3) | 96 | 116 | 1” | 1” |  |

* LKN47-VS has 1” NPT connections

Table 2  	Materials of Construction

| Material symbol | VC | VH | VS | TC | S6 |
| --- | --- | --- | --- | --- | --- |
| Part | Pump head | PVC | PVC | PVC | PVDF | SS316 |
|  | Valve ball | CE | HC | HC/SS304 | CE | HC |
|  | Valve seat | Type 32 | FKM | EPDM | SS304 | FKM | SS316 |
|  |  | Type 45 to 57 | PVC | PVC | SS304 | PVDF | SS316 |
|  | O ring | FKM | EPDM | EPDM | FKM | - |
|  | Valve gasket | PTFE |
|  | Diaphragm | PTFE + EPDM |

CE	Alumina ceramic 				EPDM	Ethylene propylene diene monomer

FKM	Fluoroelastomer				HC	Hastelloy C276

PCTFE	Polychlorotrifluoroethylene			PVC	Polyvinylchloride

PVDF	Polyvinylidenefluoride			SS316	316 stainless steel

DIMENSIONS

Outer dimensions

(	LKN32, 45, 47, 55, 57, VC, VH, VS

Dimensions in inches (mm)

| Model | L | A | C | E | F | J | K |
| --- | --- | --- | --- | --- | --- | --- | --- |
| LKN32, VC, VH, VS | 14.41 (366) | 13.78 (350) | 7.32 (186) | 4.92 (125) | 4.84 (123) | ½” NPT | 4 x ø0.35” (ø9) |
| LKN45, 47, VC, VH, VS | 14.57 (370) | 14.57 (370) | 7.40 (188) | 5.31 (135) |  |  |  |
| LKN47VS | 14.88 (378) | 8.19 (208) | 7.72 (196) | 4.09 (104) |  | 1” NPT |  |
| LKN55, 57, VC, VH, VS | 15.55 (395) | 14.57 (370) | 8.31 (211) | 4.92 (125) |  |  |  |

Outer Dimensions

(	LKN32, 45, 47, 55, 57, S6

Dimensions in inches (mm)

| Model | L | A | C | D | E | F | J | K |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LKN32, S6 | 13.27 (337) | 4.29 (109) | 3.62 (92) | 2.36 (60) | 1.65 (42) | 4.84 (123mm) | ½” NPT | 4 x ø0.35” (ø9) |
| LKN45, 47, S6 | 13.50 (343) | 5.51 (140) | 5.12 (130) | 2.36 (60) | 3.15 (80) |  |  |  |
| LKN55, 57, S6 | 15.71 (399) | 8.19 (208) | 6.30 (160) | 4.09 (104) | 4.33 (110) |  | 1” NPT |  |

# Outer Dimensions

(	LKN32, 45, 47, 55, 57, TC

| Model | L | A | C | D | E | F | J | K |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LKN32, TC | 13.27 (337) | 4.29 (109) | 3.62 (92) | 2.36 (60) | 1.65 (42) | 4.84 (123mm) | ½” NPT | 4 x ø0.35” (ø9) |
| LKN45, 47, TC | 13.50 (343) | 5.51 (140) | 5.12 (130) | 2.36 (60) | 3.15 (80) |  |  |  |
| LKN55, 57, TC | 15.71 (399) | 8.19 (208) | 6.30 (160) | 4.09 (104) | 4.33 (110) |  | 1” NPT |  |

5 Boynton Road   Holliston, MA 01746  USA  TEL:  508-429-1110    FAX:  508-429-7433    www.walchem.com